December 5th, 2007

Release Notes for MasterConsole CAT v.1.0

This document is contains the Release Notes for the MasterConsole CAT

| Effectively | Immediately |
| --- | --- |
| GA Date | December 18th, 2007 |
| Applicability | MCCAT18, MCCAT116, MCIM-PS2 |
| Firmware version | 4A0T |
| Release Status | General Availability |

Note: MCIM-USB will be GA on January 15th, 2008.

MCCAT overview

MasterConsole® CAT (MCCAT) Cat5 KVM switch is a UTP version of MasterConsole II (MCC). The OSD and user interface is the same as MCC.

The product features the use of the standard Category 5 unshielded twisted-pair (UTP) cabling. The number of the accessible computers can expand to a maximum of 256 computers with a two-tier cascaded system.  The connections between servers and MasterConsole CAT are thru CAT5. The maximum resolution and distances supports 1280x1024 resolutions in 150 feet and 1600x1200 in 100 feet.

It also provides MasterConsole Computer Interface Module (MCIM) to connect PS/2 and USB interface servers under different platforms. It works with every leading server: Microsoft Windows NT, Windows Me, Windows 2000, Windows XP, Windows 2003, Windows Vista, Novell NetWare, UNIX and Linux

In terms of operation, the product provides front panel buttons for easy and fast access to the attached computers in addition to a friendly OSD interface for simple system configuration.

Compatible CIM list (by priority):

1. MasterConsole CIM:PS/2, USB (cascade, directly connect)

2. Dominion CIM: PS/2, USB (directly connect)

3. Paragon II ACIM: PS/2, USB (directly connect)

4. Paragon II CIM: PS/2, USB, P2CIM-SER (directly connect)

Compatible KVM Switches

MasterConsole II : MCC8  and MCC16 as the 2nd tier

Important Notes and Information

- Limitations:

Console port only supports PS/2 keyboards and mice. Using PS/2 adapter to connect the USB keyboard is working but not guarantees totally support.

For the best possible video quality, adhere to these distance guidelines from the MCIM to MCAT

| Server Video resolution | Distance |
| --- | --- |
| 1280x1024 (and below) | 150 feet |
| 1600x1200 | 100 feet |

II. Know Issues and CRs.

For this release, listed below are known issues that are being worked on for future MasterConsole CAT firmware release.

- Random (rare occurrence) : Switching into the 2nd tier's channel (RS6000) and type characters and move the mouse quickly sometime the code set was wrong.

How to fix: The two ways can fix the issue

1.Switching the same channel again if the user can enable the OSD

2.Plug out and plug in the Local keyboard or Reboot the Base MCCAT

- Press <F8> Upgrade PC Status the OSD menu one word color is wrong

How to fix: Press the Page up or Page down can fix the issue

- Random (rare occurrence): use MCUpdate to update MCCAT URKVM F/W and switch channel sometime KB/MS can't work.

How to fix: Reboot the base tier can fix the issue

- Random (rare occurrence): The Previous Key set the"LefAlt" sometime switching into the 2nd tier would lose the LftAlt break code

How to fix: Pressing the LftAlt again can fix the issue

- Random:Sometime switch into the 2nd tier's channel and the channel's keyboard and mouse can't work

How to fix: Waiting the Keyboard timeout then switching the same channel again

- Random (rare occurrence):Sometime switch into the 2nd tier's channel then the keyboard can't work

How to fix: Plug out and Plug in the local keyboard can fix the issue

- Random (rare occurrence):The MCCAT use the UKB-12 keyboard sometime has the typematic issue.

How to fix: It only happens on The Microsoft Natural Keyboard Pro randomly but cannot be fixed.

MCCAT18/116 Release Notes, Revision 1.0 Dec 5, 2007

This note is intended for Raritan customers only; its use, in whole or part, for any other purpose without the express written permission from Raritan Computer, Inc. is prohibited.

Copyright ©2007 Raritan Computer, Inc. CommandCenter, Dominion, and the Raritan company logo are trademarks or registered trademarks of Raritan, Inc. All rights reserved. Solaris and Java are trademarks of Sun Microsystems, Inc. Windows and Windows Vista are trademarks or registered trademarks of Microsoft Corporation. Mac and Safari are trademarks or registered trademarks of Apple Inc. All other marks are the property of their respective owners.